## Slide 1: StarAngle: User Orientation Sensing with Beacon Phase Measurements of Multiple Starlink Satellites
Raghav Rathi and Zhenghao Zhang
Department of Computer Science
Florida State University
USA

## Slide 2: Starlink Satellites
Over 6000 now
Will reach 42000

## Slide 3: Starlink Satellite Beacons
This Photo by Unknown Author is licensed under CC BY-SA
Beacon is a pure sinewave (some around 11.95 GHz)
Each satellite transmit multiple beacons separated by 43945 Hz
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 4: Advantages of Using Starlink Beacons
Global coverage
Free (no need to install base stations)
Line of Sight path from the satellite (no multipath)

## Slide 5: Used in User Localization
Sharbel Kozhaya, Haitham Kanj, and Zaher M. Kassas. 2023. Multi-Constellation Blind Beacon Estimation, Doppler Tracking, and Opportunistic Positioning with OneWeb, Starlink, Iridium NEXT, and Orbcomm LEO Satellites. In 2023 IEEE/ION Position, Location and Navigation Symposium (PLANS). 1184–1195
Sharbel E. Kozhaya and Zaher M. Kassas. 2023. Positioning with Starlink LEO Satellites: A Blind Doppler Spectral Approach. In 2023 IEEE 97th Vehicular Technology Conference (VTC2023-Spring). 1–5.
Chun Yang and Andrey Soloviev. 2023. Starlink Doppler and Doppler Rate Estimation via Coherent Combining of Multiple Tones for Opportunistic Positioning. In 2023 IEEE/ION Position, Location and Navigation Symposium (PLANS). 1143–1153.

## Slide 6: User Orientation
Sometimes the GPS does not know the direction until we start driving

## Slide 7: StarAngle

## Slide 8: StarAngle
Measure the beacon phase difference
Phase difference is a function of the angle connecting the centers of the LNBs
Commodity LNBs have internal clocks not synchronized with each other
θ(t)
N
S1

## Slide 9: Our solution
Receive from multiple satellites simultensously
The clock difference is cancelled
Θ(t) = θ1(t) - θ2(t)

## Slide 10: Challenges
Signal can be very weak (-30 dB)
Frequency change due to motion (-4 kHz per second)

## Slide 11: StarAngle
This Photo by Unknown Author is licensed under CC BY-NC
Satellite Detection
Phase Measurement
Orientation Estimation

## Slide 12: Satellite Detection
Use the Doppler Rate (frequency change rate) to match detected satellites to known satellites

## Slide 13: Starlink Satellite Information
Maintained by celestrak
Two Line Elements (TLE)
STARLINK-31569
1 59857C 24097Y 24171.41993056 .00000659 00000+0 15714-4 0 1711
2 59857 42.9992 252.7558 0001247 264.8185 17.8746 15.40707837 19

## Slide 14: Finding Satellite Motion Parameters
Doppler rate: dopplershift function in Matlab
Azimuth and Elevation angles: the aer function in Matlab

## Slide 15: Dealing with Very Weak Signal with Unknown High Doppler Rate
Divide the signal into 10-ms segments
Do a linear scan of Doppler rates from -10, -9, …, 9, 10 kHz
Add the FFT up. When Doppler rate roughly match, will see a peak

## Slide 16: Typical Results
The measured Doppler rate matches the one calculated by TLE very well
The Doppler rate can vary

## Slide 17: Phase Measurements
Pick the strongest beacon and use a Low Pass Filter of 100 Hz wide to obtain the time-domain signal

## Slide 18: An example
Processed performed every one second
Need to dechirp first (cancel Doppler rate)

## Slide 19: Typical Results
Phase measurement and calculation based on TLE usually match very well

## Slide 20: Orientation Estimation
Use (Az,El) as input and try possible values of angles and use the one best match the measurement

## Slide 21: Phase Calculations

## Slide 22: Cost Function

## Slide 23: Evaluation

## Slide 24: Estimation Accuracy

## Slide 25: Phase Measurement

## Slide 26: Experiment Information

## Slide 27: Experiment Analysis

## Slide 28: Self Average

## Slide 29
This Photo by Unknown Author is licensed under CC BY-NC